## Slide 1: Simulation of a complete 5g environment
Using Open5GS and UERANSIM
Presentation for Mobile Computing (WS2023-24) by TeamSliceX
M.Eng in Information Technology
Date: 22.02.2024

## Slide 2: INTRODUCTION
Our project aims to simulate the flexibility and adaptability of a 5G network by implementing network slicing. It involves deploying a 5G Stand Alone network using Open5GS as the core and UERANSIM for the 5G-RAN.
The main objective is to enable network slicing for File Sharing, Streaming, and VOIP calling services for two tenant groups. Due to software limitations, Open5GS and SRSRAN were replaced with UERANSIM for network slicing.
Kamailio, Next Cloud, and JellyFin servers were configured separately for VOIP Calling, File Sharing, and Video Streaming services.
Link to our repository in github: https://github.com/FRA-UAS/mobcomwise23-24-teamslicex

## Slide 3: MEET OUR TEAM
Mashnunul Huq
(1384042)
Anurag De
(1400450)
Sourav Paul Sumit
(1344118)
Erdi Tras
(1427187)

## Slide 4: Primary components
Open5gs
Open5GS is an open-source project aimed at implementing a 5G mobile core network using C-language.
It aims to enable 5G Core network functions and is designed to be interoperable with existing network infrastructure.
Open5GS provides interfaces for integration with legacy 4G/LTE networks and interconnecting with external networks and services.
Acts as the control plane of the 5G core network of our project.
UERANSIM
UERANSIM is an open-source implementation of the User Equipment (UE) side of the 5G Radio Access Network (RAN), developed as part of the OpenAirInterface project, which comprises of multiple UEs and gNB.
It simulates the behavior of a 5G UE, allowing developers, researchers, and network operators to test and experiment with 5G networks in a controlled environment.
It can be integrated with third-party core network solutions to build complete end-to-end mobile wireless networks.

## Slide 5: Other tools used
VirtualBox
Oracle's VirtualBox is an open-source virtualization software that enables simultaneous running of multiple operating systems on a single physical machine. It supports various host operating systems and guest OSes, including Windows 11, Linux, and Solaris.
Linphone
To support VoIP calls, the Linphone v4.4.21 was installed in the end user UERANSIM VM’s where GNB and UEs are situated.
Kamailio
Wireshark
For SIP VoIP Calling, Kamailio v5.5.1 is installed in the system. This feature will provide a SIP calling service for desired network slice.
To simulate a file sharing platform, NextCloud v28 is installed.
NextCloud
For traffic collecting and analysis, the required LXC container has Wireshark v3.2.3 installed as a packet capture tool.
JellyFin
To achieve video streaming services, JellyFin v10.8.13 is installed in first UE of the Kamailio server setup.

## Slide 6: Key theoretical concepts

## Slide 7: 5G CORE
The 5G Core (5GC) is the central intelligence of a 5G network, managing data traffic, connecting with User Equipment (UE), providing essential network services, and enhancing security measures.
It consists of two functional planes: the Control Plane and the User Plane, which operate independently for flexible scalability and dynamic deployments. The User Plane consists of UE, Radio Access Network, and User Plane Function (UPF), while the Control Plane includes functions like Access and Mobility Management Function (AMF) and Session Management Function (SMF).
Open-source projects like Open5gs are used for implementing 5G Stand-Alone networks.

## Slide 8: RADIO ACCESS NETWORKS (RAN)
Radio Access Network (RAN) plays a vital role in wireless communication systems, establishing radio connections between individual devices and different parts of the network.
Facilitates connections between devices like cellphones, computers, or remotely controlled machines.
This project focuses on connection experimentation using UERANSIM, an open-source project consisting of gNodeB and UE. gNodeB manages user traffic on simulated radio links, while UE acts as a subscriber.
UERANSIM works perfectly with Open5GS, unlike srsRAN, which has compatibility issues with Open5GS Core.

## Slide 9: RADIO ACCESS NETWORKS (RAN)
Network Slicing is a key technology in the 5G era, allowing the sharing of a single telecommunication network infrastructure by multiple logical networks, known as network slices.
It enhances the flexibility, efficiency, and security of 5G networks, allowing them to cater to various service requirements.
Network slices can support mobile broadband applications within one slice and dedicate another slice to specific non-mobile applications, all using shared physical resources. Virtualization technologies like Software-Defined Networking (SDN) and Network Function Virtualization (NFV) enable 5G network operators to create customized networks tailored to specific functional, QoS, and user-specific requirements.
Network slicing enables the creation of numerous virtual networks on a shared physical infrastructure, allowing for efficient and interactive resource utilization.

## Slide 10: Architecture Designs of our project

## Slide 11
VM 5
Open5GS 5GCore Core-Plane
IP: 192.168.100.4-6/24
Open5GS 5GCore User-Plane1
IP: 192.168.100.11/24
Open5GS 5GCore User-Plane2
IP: 192.168.100.12/24
VM 4
UERANSIM
gNodeB
IP: 192.168.100.20
AMF
IP:192.168.100.4
SMF1
IP:192.168.100.5
SMF2
IP:192.168.100.6
UPF 1
UPF 2
VM 1
VM 2
VM 3
When
uesimtun0/
10.45.0.2
SST=1
SD=0x000001
SST=1
SD=0x000002
Service Based Interface
127.0.0.5
127.0.0.4
127.0.0.24
UERANSIM
gNodeB
IP: 192.168.100.21
IMSI-001010000000001
When
Uesimtun0/
10.46.0.2
UERANSIM
UE
IMSI-001010000000000
NextCloud
IP:192.168.100.(4-6)/24
Architectural design of 5G network for File Sharing and internet pinging using Open5gs & UERANSIM

## Slide 12
VM 4
VM 5
Open5GS 5GCore Core-Plane
IP: 192.168.100.21-23/24
Open5GS 5GCore User-Plane1
IP: 192.168.100.31/24
Open5GS 5GCore User-Plane2
IP: 192.168.100.32/24
UERANSIM
gNodeB
IP: 192.168.100.33
AMF
IP:192.168.100.21
SMF1
IP:192.168.100.22
SMF2
IP:192.168.100.23
UPF 1
UPF 2
VM 1
VM 2
VM 3
When
uesimtun0/
10.47.0.2
10.49.0.2
SST=1
SD=0x000001
SST=1
SD=0x000002
Service Based Interface
127.0.0.5
127.0.0.4
127.0.0.24
UERANSIM
gNodeB
IP: 192.168.100.34
IMSI-001010000000001
When
Uesimtun0/
10.48.0.2
10.50.0.2
UERANSIM
UE
IMSI-001010000000000
Kamailio
IP:192.168.100.24/24
Architectural design of 5G network for VoIP Calling and Video Streaming using Open5GS & UERANSIM
JellyFin http://192.168.100.33:8096
SST=2
SD=0x000004
SST=2
SD=0x000003

## Slide 13: Architecture Explanation:
All network components are configured in different VMs
Four UEs were created in separate VMs. We have provided separate slicing to individual User Equipment to access the File sharing, streaming and VoIP calling services. The corresponding details of services are available to a particular UE.
As per the project requirement UE1 and UE2 (of MultiVMApproach Folder Configuration in GitHub) have access to File Sharing, UEConfigs and UEConfigs2 (of MultiVMForKamailioServer Folder Configuration in GitHub) have VoIP calling service, UE3 and UE4 (of MultiVMForKamailioServer Folder Configuration in github) Streaming services and associated with UPF-1 and UPF-2. UE3 and UE4 have access to VoIP calling service and associated with UPF-3 and UPF-4. Then UE5 and UE6 have access to VoIP calling service and associated with UPF-3 and UPF-4.
Each of the four SMF files are used for network slice selection as per the slicing parameters provided by the UEs.

## Slide 14: Architecture Explanation:
The data network consists of NextCloud server for providing File sharing service to UE1 and UE2 installed in MainCore VMs corresponding to MultiVMApproach Folder Configuration in github. JellyFin server for providing live streaming service to UE5 and UE6 installed in MainCore2 VMs corresponding to MultiVMForKamailioServer Folder Configuration in github. Kamailio server for providing VoIP calling server to UE3 and UE4 installed in MainCore2 VMs corresponding to MultiVMForKamailioServer Folder
Each slice is associated with the different Data Network subnet to access services.
We have used standard 5QI values for providing the File sharing, streaming and VoIP

## Slide 15: LIMITATIONS of our project:
It is found in the implementation process of srsRAN that ZMQ (virtual radio in srsRAN) only support a single eNB and a single UE.
To run more than one user equipment, multiple UE/gNB pairs are required to setup in different VMs.
In the configuration of UERANSIM and Open5GS more than one SST value is at the beginning of the project was not supported. Later Open5GS developers fixed it and now both SST and SD values are probable separation technique for sessions now.

## Slide 16: Thank you
Now, lets move to live demonstration of our project​.